## Slide 1: Ultrasonic Radar System
Hardware Architecture & Software Visualization
Arduino Uno + Python + HC-SR04

## Slide 2: Project Overview
A complete radar scanning system built in two parts:
  1. Sensor Node (Arduino): Controls a servo motor and reads an ultrasonic sensor.
  2. Processing Node (Python): Ingests serial data to render a live polar display.

## Slide 3: Hardware Setup
Wiring Guide:
  Servo (SG90):
    Red -> 5V | Brown -> GND | Orange -> Digital Pin 9
  Ultrasonic Sensor (HC-SR04):
    VCC -> 5V | GND -> GND | Trig -> Digital Pin 10 | Echo -> Digital Pin 11

## Slide 4: Firmware Logic (C++)
The Arduino sweep function limits angles to 15-165 degrees to avoid mechanical stress constraints on the servo.
Code Snippet:
  for(int i=15; i<=165; i++){ myServo.write(i); delay(30); distance = calculateDistance(); Serial.print(i); Serial.print(","); Serial.println(distance); }

## Slide 5: Calculation Logic
The distance is formulated by triggering the sensor and listening for the echo.
Code Snippet:
  digitalWrite(trigPin, HIGH); delayMicroseconds(10); digitalWrite(trigPin, LOW); duration = pulseIn(echoPin, HIGH); // Speed of sound = 340 m/s = 0.034 cm/us distance = duration * 0.034 / 2;

## Slide 6: Software GUI & Processing (Python)
Key techniques applied in Python visualization:
  Polar Graphics: Uses matplotlib to map spherical coordinates (r, theta) into a realistic radar plot.
  Alpha Filtering (Moving average): smooths out sensor noise: distances[idx] = (0.7 * current) + (0.3 * previous)
  Persistence: Applies an alpha decay frame-by-frame for trailing radar effect: alphas[alphas > 0] -= 0.03